- Hardware
  - wiring
    - power
    - motor power, encoder
    - Digital IO:
      - Servo enable: X5
      - Servo Homing: X4
  - network
    - Moons motor: IP: 192.168.0.140
    - Jetson Nano: IP: 192.168.0.75
- MODBUS For Moons Motor
  - Registers used
  - Status Code and Alarm Code
  - Register 125 Opcode

- Sequence of operation
  - Homing
    - Registers used and value to write
    - Timing Diagram
  - Manual Jog
  - Auto position mode
- PLC Handshake
  - DB
    - Trigger bits
    - alarm code
    - status code
    - heartbeat signal
- Python Program
MODBUS For Moons Motor
Registers Used

Register	Access	Data Type	Description
40001	Read Only	SHORT	Alarm Code (AL) 16 bit
40002	Read Only	SHORT	Status Code (SC)
...	...	...	...
40030	R/W	SHORT	Velocity (VE)
40031..32	R/W	LONG	Point-to-Point Distance (DI)
...	...	...	...
40049	R/W	SHORT	Jog Velocity (JS)
...	...	...	...
40125	R/W	SHORT	Command Opcode
40126	R/W	SHORT	Parameter 1
40127	R/W	SHORT	Parameter 2

Alarm Code:

The alarm code is used to indicate the current alarm information of the drive. Each bit of the alarm code register represents different alarm information,when a bit is set1.

Register 40001:

Bit	Desciption
0	Position error overrun
1	CCWDirection prohibition limit
2	CWDirection prohibition limit
3	drive over temperature
4	Drive internal voltage error
5	Drive overvoltage
6	Drive undervoltage
7	Drive overcurrent
8	Motor winding switch
9	Motor encoder signal error
10	Communication exception
11	Failed to save parameters
12	Command the motor to run when it is not enabled
13	Motor overload status
14	calledQblock is empty
15	memory error

Status Code:
Status code is used to indicate the current working status of the drive. Each bit of
the status code register represents different status information,when a bit is set1.

Register 40002:

Bit	Desciption
0	Enable
1	Sampling (The software oscilloscope function is enabled)
2	Drive reports failure
3	Movement in place
4	in motion
5	jogging running
6	decelerating
7	waiting for input signal (e.g. execute WI instruction)
8	parameter saving
9	drive warning
10	back to origin
11	waiting time (e.g. execute WT,WD instruction)
12	internal use
13	Encoder detection
14	Qprogram is running
15	Initialization (step system), Servo ready (Servo system)

Command Opcodes:

Certain actions are executed based on the value of the corresponding opcode written in the register.

Register 40125:

Function	Opcode	Parameter1	Parameter2
Alarm Reset	0xBA	x	x
Start Jogging	0x96	x	x
Stop Jogging	0xD8	x	x
Feed to Length	0x66	x	x
Feed to Position	0x67	x	x
Motor Disable	0xA3	x	x
Motor Enable	0xA2	x	x
Seek Home	0x6E	I/O Point	Condition
Stop Move & Kill Buffer, / Max Decel	0xE1	x	x
Stop Move & Kill Buffer, / Normal Decel	0xE2	x	x

Sequence of Operation
Homing

Homing is performed initially after turning the drive of the motor on. This sets the encoder value as zero in the desired position based on the sensor input.

To perform homing, we need to provide a sensor input to the X04 input of the drive and set the condition parameter as signal falling edge indicating that the homing is complete when the sensor input turns on. Homing operation is performed when the desired opcode trigger is set to the opcode register.

I/O instruction Code:

Hex	Desctiption
0x31	Digital input/output ports 1
...	...
0x36	Digital input/output ports 6
0x37	Digital output port 7
...	...
0x3c	Digital output port 12
0x52	Signal rising edge
0x46	Signal falling edge

Python Function:
def seekHome():
   writeRegister(125, 0x34, 1)
   writeRegister(126, 0x46, 1)
   writeRegister(124, 0x6e, 1)
   while True:
       x,y=getStatus(1)
       if 10 not in y:
        break

This function sets register 40126 as 0x34 indicating the sensor is connected to digital input port 4 and register 40127 as 0x46 indicating the signal is falling edge. Next, opcode 0x6e (Seek Home) is set to opcode register 40126 driving the motor towards the positive direction (Clockwise) until the sensor input is high. Once the sensor input turns on, the motor stops rotating and the encoder value is set as zero. You may note that status monitoring is done in the while loop of the program. It waits for the bit 10 to be low in the status code indicating the the homing sequence is comlete only after which the function is exited.

Note: When the message is read and written, Pay attention to the conversion relationship between register addresses,as register 40125 converted to 0x007C,
which is 40125-40000-1=124(0x007C)

Manual Jogging

manual jogging is performed to rotate the motor in either clockwise or counter clockwise direction by pressing the specified pushbutons in the manual mode.

To perform manual jogging, we need to set the jog speed of the motor with appropriate sign convention for required direction. On providing the motor with start jog trigger in the opcode register, the motor starts to jog.

  - Homing
    - Registers used and value to write
  - Manual Jog
  - Auto position mode

stopJog()
def stopJog():
    writeRegister(124, 226, 1)
    print("Jog Stopped")

resetAlarm()
def resetAlarm():
    writeRegister(124, 186, 1)

setPosition()
def setPosition(pos,speed, ids):
    longWrite(30,pos, ids)
    writeRegister(29,speed,ids)
    writeRegister(124, 0x67, 1)

seekHome()
def seekHome():
    writeRegister(125, 0x34, 1)
    writeRegister(126, 0x46, 1)
    writeRegister(124, 0x6e, 1)
    while True:
        x,y=getStatus(1)
        if 10 not in y:
        break

setSpeed()
def setSpeed(speed, ids):
    writeRegister(48, speed, ids)

startJog()
def startJog():
    global motor_status
    writeRegister(124, 159, 1)
    writeRegister(124, 150, 1)
    print("Jog started")

readAlarm()
def readAlarm(ids):
    #val1= readRegister(0, ids,0)
    #val2= readRegister(1, ids,0)
    val= readRegister(0, ids,0)
    # print("Alarm Value: ",val)
    alarms= {0:"position error overrun", 1:"reverse prohibition limit", 2:"positive prohibition limit", 3:"over temperature", 4:"internal error", 5:"supply voltage out of range", 6:"reserved", 7:"drive overcurrent", 8:"reserved", 9:"motor encodeer not connected",
        10:"communication exception", 11:"reserved", 12:"vent failure", 13:"motor overload protection", 14:"reserved", 15:"unsuaal start alarm"}

    error= getBits(val,16)

    for i in error:
        print(alarms[i], end= ", ")

    return val, error

getStatus()
def getStatus(ids):
    val= readRegister(1, ids,0)
    # print("Status Code: ", val)
    lst= getBits(val,16)
    return val, lst